SYSTEMATIC JOURNALING OF

COMMUNITY DEVELOPMENT CENTER

1. The content of the article is the result of the activities of the community which have been carried out, generally in the form of the application of science technology, economy, education, health, the environment, and the arts.

2. Articles are written in the Indonesian Language, format one column using arial font size 11 pts, 1.5 spacing, printed out on paper As many as 10 to 15 A4 pages.

3. Systematics of the article as follows:

a. Title (capital letters, size 12 pts, maximum 20 words).

b. Noted author name (maximum 3 persons, without academic degree), the Faculty and the email address of the author. Written with the letter arial size 10 pts, 1 spaces.

c. Abstract (in United Kingdom and Indonesia are written 1 spacing, size 10 pts, arial italic, and maximum I50 words).

d. Keywords (taken from the title or abstract).

e. Introduction (contains lalar back, problem, purpose, benefits, and a review of the literature, without subtitles).

f. Method (contains the steps that are used to resolve the problem, including the language, tools, evaluation is conducted and statistics to analyze the data).

g. Results and Discussion (containing the results of the activities performed and the discussion of the results, the share of the writing in this section at least 2 pages).

h. Conclusions and suggestions (Conclusions Contains the answer to the problems raised, while the Suggestions it contains advice that relates to conclusions).

i. Bibliography (contains the libraries cited and used in the writing).

5. Referrals/excerpts using parentheses (name, year, and page) or when placed in front of the name (and page).

6. Pictures and photos relating to the activities of the devotion encouraged included in the article.

7. Table and Figure should be numbered (Arabic numerals) and the title, as well as a description of the clear. The title of the table is placed on the top of the chart, while the title of the picture is placed below the image. The table using only horizontal lines, with no vertical lines.

8. Bibliography written sequential alphabetically based on what format the style, in the order: author's name (last name before). Of the year. the title of the book (italic). City: Publisher. Example: Haryoto. 1996. Create bamboo chairs. Yogyakarta: Kanisius.

EXAMPLE Of WRITING JOURNAL ARTICLES P2M

SOCIALIZATION & USE TRAINING

OSCILLOSCOPE SIMULATOR version 1

1)Darwin Sebayang, 2)Nurato 3)Nur Indah

Program Studi Teknik Mesin, Fakultas Teknik, Universitas Mercu Buana Jakarta

Email: d_sebayang@hotmail.com, nuratoa@gmail.com, nur.indah@mercubuana.ac.id

Abstract

The oscilloscope Simulator is a software that is used to introduce to users on the basis of an electrical signal measurement system using the oscilloscope. The oscilloscope Simulator can be used to train users in the actual operation of the oscilloscope. The performance of the instruments in the oscilloscope Simulator along with components and the buttons are resembles the actual form of the instrument. Community service activities conducted at SMK Negeri 35 West Jakarta were attended by 25 students and 1 Guru in class XII Audio Video study Program, the activities took place by introducing a direct oscilloscope simulator to students with Presentations and practice using simulators.  The activity was terminated by giving 1 CD the oscilloscope Simulator with 1 module how to use.

Keywords: Oscilloscope, oscilloscope Simulator

1. INTRODUCTION

1.1. Background

The oscilloscope is an electronic measuring instrument that can project a signal form both an analog signal and a digital signal so that the signals can be seen, measured, calculated and analyzed according to the desired signal output form ( Rian Priyadi, 2013). The oscilloscope plays a very important role in the field of technological development because to create an electronic device it takes a measuring instrument that can be used to analyze the device to be made so that the device Can work as desired by the author.

But the oscilloscope is a measuring instrument that is not cheap, so not everyone can buy the device. This will be an obstacle for those who work in the field of electronics, students and students who study the field of electronics, as well as those who have a hobby in the field that has enough to own the device.

So it is the background of the author to introduce a tool that serves as an oscilloscope with a cheaper price, practical (easy to use, and easy to carry) and shaped as an application (software) or Virtual instumentation.

1.2. Focus on Community Devotion

SMK Negeri 35 has the direction of Audio video, electrical engineering and mechanical Engineering, where 3 (three) majors use the measuring instrument of the oscilloscope to do the practice on the subjects of electrical engineering. The obstacles faced were the lack of the oscilloscope measuring instruments in the school laboratory.

To have an oscilloscope in addition to the price that must be issued is not cheap, use and maintenance of the oscilloscope should be a concern, because as an electronic device oscilloscope has a high level of sensitivity to the inputs which can sometimes make the oscilloscope become corrupted.

Because the oscilloscope is a virtual oscilloscope, so the users are students, students and professionals will be more easily understand the work of the oscilloscope without any fear of the wrong relationship of electronic compenen or damage On the oscilloscope.

1.3. Justification and objectives

The oscilloscope measuring instrument is a very necessary device in the field of electronics, especially in the world of education as a tool of practicum and measurement, but generally the device is not cheap so it will be an obstacle, school, campus or an educational institution is only able to buy 1 to 2 oscilloscope to be used as props.

With the use of this virtual oscilloscope, students are expected to learn the work process, how to capture data, measurement and read the measurement results easily without any fear of damage when there is a validity of the adjustment.

1.4. Problem identification

From the identification of the problem, there are several important points, including:

- The oscilloscope measuring instrument is a very necessary device in the field of electronics but not cheap, so it becomes an obstacle for people who need it but do not have enough financial to buy it.

- The oscilloscope has high sensitivity so often in its use or doing practicum an error occurs resulting in damage to the appliance.

- Not very few people working on mobile and need an oscilloscope gauge to get the job done, but the devices that are easy to carry and portable are more expensive.

1.5. Relevance

The Virtual oscilloscope is a research in order to support the equipment in the UMB Mechanical Laboratory, which is now still in Phase 1 and continues development. This Phase 1 virtual oscilloscope is still around the way of use, the working process of the oscilloscope to the way the output signal is measured.

2. METHOD

The methods of implementing activities are divided into 4 parts:

2.1. Pre-Tes

Pre-test activities conducted before the training activities were given, students have not read the instruction manual on the use of the Virtual oscilloscope or the material relating to other oscilloscope, nor try to operate the virtual oscilloscopes. Pre-Test to find out where the student knowledge of the oscilloscope measuring instruments and the ability to use the oscilloscope.

2.2. The author

The briefing is to provide an overview of:

1. Oscilloscope measuring instrument.

2. oscilloscope components.

3. The functions of the existing components.

4. How to operate, turn on and off the oscilloscope.

5. Connect the oscilloscope with the tools to be measured.

2.3. Training implementation

Training is conducted with the following stages:

1. The virtualization of the virtual oscilloscope software.

2. Running virtual oscilloscope software.

3. Calibrate.

4. Performs voltage and frequency measurements.

2.4. Post–Test and Kuestioner

Post-Test activities are conducted after training activities are given, students have read the user manual for using the virtual oscilloscope or materials related to other oscilloscope, and training execute the virtual oscilloscope. Kuiser is conducted to determine the extent to which the virual oscilloscopes provide ease and understanding to the students and teachers in conducting practicum-practicum related to the oscilloscope measuring instruments.

3. RESULTS AND DISCUSSION

3.1.  Result

| No. | External Type | Product Indicators |
| --- | --- | --- |
| 1 | Scientific publications in journals/proceedings ISSN ber 1) |  |
| 2 | Publications in mass media print/online/repocitory PT 6) |  |
| 3 | Increased competitiveness (improved quality, quantity, and value added goods, services, product diversification, or other resources) 4) |  |
| 4 | The increased application of science and technology in society (mechanization, IT, and management) 4) |  |
| 5 | Improvements to the corporate values of society (arts and culture, social, political, security, peace, education, health) 2) |  |
| 6 | Publications in international journals 1) |  |
| 7 | Services, social engineering, methods or systems, product/item 5) |  |
| 8 | New innovation TTG 5) |  |
| 9 | Intellectual property (patents, Copyright, simple Patent, trademark, trade secret, Industrial product design, plant breeders ' rights, Design protection for Integrated Circuit Topographies) 3) |  |
| 10 | Stylish book ISBN 6) |  |

3.2. Discussion

In order to do devotion, it is important to introduce this Virtual oscilloscope to the community especially vocational high school students who are in practical learning, then we offer a solution that may be found in Application of the Oscilloscope tools as follows:

1. The appearance of the instruments in the oscilloscope simulators with components and the buttons are resembles the actual form of the instrument.

2. The oscilloscope Simulator can be operated in the same way as the actual use of the instrument such as plugging the plug into the power outlet, turning it on by pressing the ' ON/OFF ' button, and rotating or pressing the buttons on the panel.

3. The oscilloscope Simulator can be operated freely and does not need to follow the specified Urut-urutan so that the user can gain such experience when operating the actual instrument.

4. Students can easily understand the work process of the oscilloscope.

5. Students can use the virtual oscilloscope to train users in the actual operation of the oscilloscope.

4. CONCLUSIONS AND SUGGESTIONS

From the proceeds of devotion in SMK Negeri 35 then can be saved

1. The oscilloscope Simulator is indispensable to learners before performing the measurements using the actual oscilloscope.

2. The oscilloscope Simulator will facilitate students to understand the functions of each component in the Simulator.

BIBLIOGRAPHY

Najaruddin. 2014. Osiloskop, Education. Universitas Muhammadiyah Prof. Dr Hamka, Jakarta.

Stevani Agnesia Sigiro. 2015. Instrumentasi Virtual Menggunakan Labview Dan Soundcard. LIPI Indonesia.

Wulan Sari. 2013. Alat Ukur dan Teknik Pengukuran, jilid 2. Jakarta: BSE.